## Slide 1: Precision Ag and Conservation
Precision Ag Technologies are most often developed to increase efficiency and decrease input cost
However, they provide great opportunity for soil and water conservation
Technologies may be used to indirectly map soils at high resolution?

## Slide 2: Yield Maps
What controls Yield???
  Nutrient availability
    Organic matter, clay content, and type
  Plant available water holding capacity
    Depth, texture, horizonation, and organic matter content
  Soil aeration
  Pest pressures
  pH, salinity
A soil map should tell us many of these things

## Slide 3: Yield Maps
Some times they can be useful
  If soil mapping unit is uniform
  If there are biologically (influential on yield) significant differences between mapping units in a field
Sometimes soil maps provide very little explanation of yield variability
  Heterogeneous mapping units
  No biologically significant differences between mapping units.
An understanding of soils and how they are mapped can be useful in interpretation

## Slide 4: Soil Survey map
The whole field is a Taloka silt loam, which is a highly variable mapping unit

## Slide 5: Range of Soil Characteristics for the Taloka
Depth to Redoximorphic features (indicator of wetness)=6-14 inches
Depth to clay pan=28-48 inches
Clay content=30-60%
Excellent example of a mapping unit that provides limited information for precision management.
Every acre can easily be different.

## Slide 6: Relationship Between Limiting Layer and Yield (Ottowa Co)
Limiting layer is defined as the layer with a clay content above 35%, containing Redoximorphic features (drainage problem)
The high yielding outliers indicate that much of the field is under managed
Problems with:
  Nutrients
  pH
  Salinity
Chart: Depth to limiting layer
| 16.929133858267644 | 23.5 | 25 | 18.5 | 23.25 | 9 | 22 | 19 | 22 | 19 | 21.653543307086615 | 14
 | 40 | 34 | 40 | 25 | 55 | 12 | 33 | 19 | 29 | 25 | 54 | 21

## Slide 7: Soil Map, Ponca City
A little bit!
Port Silt loam is a beautiful Alluvial soil
The Tabler and Kirkland aren’t bad but they’re not Ports

## Slide 8: Relationship Between Limiting Layer and Yield
Restrictive layer was defined as a firm layer with a clay content greater than 35%, and a color value greater than 2.
The color component accounts for the very dark brown subsoil in the Port silty clay loam
This Port did have clay
greater than 35% but
organic matter content
and landscape position
prevented yield limitation
Chart: Depth to Restrictive Layer (in)
| 31.889763779527556 | 13.385826771653544 | 13.77952755905512 | 29.527559055118111 | 33.070866141732267 | 12.204724409448819 | 24.015748031496063 | 35.826771653543297 | 14.566929133858268
 | 39.6314 | 31.5774 | 21.526 | 40.7551 | 52.5397 | 25.0188 | 31.8682 | 37.7462 | 21.669

## Slide 9: Soil Test P, Ponca City

## Slide 10
Chart: 
| 39 | 32 | 26 | 46 | 19 | 41 | 26 | 18 | 25 | 24 | 28 | 33 | 32 | 25 | 43 | 13 | 42 | 29 | 27 | 34 | 28 | 28 | 31 | 33 | 19 | 32 | 37 | 40 | 46 | 57 | 29 | 42 | 47 | 37 | . | 33 | 10 | 18 | 41 | 24 | 44 | 37 | 41 | 47 | 25 | 25 | 17 | 29 | . | 65 | 29 | 34 | 37 | 37 | . | .
P vs Yield | 26.502 | 28.3046 | 15.1482 | 28.7708 | 16.4776 | 18.9873 | 19.3191 | 13.7738 | 21.1613 | 15.6311 | 31.6131 | 24.2881 | 19.9864 | 27.6092 | 35.4026 | 15.2112 | 27.6829 | 27.8692 | 24.9446 | 17.9604 | 16.7247 | 34.2683 | 22.2784 | 24.8761 | 21.4159 | 34.3652 | 19.9446 | 29.287 | 24.3787 | 18.3822 | 24.1105 | 29.5384 | 32.229 | 27.2154 | 36.6246 | 39.9605 | 17.4064 | 19.1751 | 28.1367 | 29.9983 | 25.6549 | 24.6641 | 24.0368 | 25.0619 | 21.0748 | 23.1831 | 23.93 | 27.1174 | 43.7705 | 47.8111 | 24.5914 | 30.377 | 34.5555 | 30.7543 | 27.2668 | 24.2079

## Slide 11: pH, Ponca City

## Slide 12
Chart: 
| 5.9 | 5.8 | 5.6 | 5.4 | 5.5 | 5.3 | 6.8 | 5.7 | 5.2 | 5.6 | 5.6 | 5.7 | 5.4 | 5.8 | 5.4 | 6.1 | 5.3 | 5.5 | 5.4 | 5.0999999999999996 | 5.7 | 5.8 | 5.7 | 5.4 | 5.7 | 5.5 | 5.7 | 6.5 | 5.5 | 5.9 | 5.3 | 5.6 | 5.6 | 5.3 | 5.6 | 5.5 | 6.3 | 5.9 | 6.4 | 5.5 | 5.4 | 5.6 | 5.4 | 5.5 | 5.6 | 5.8 | 5.6 | 5.6 | 7.5 | 7.3 | 5.5 | 5.4 | 5.4 | 5 | 5.4 | 6.1
pH vs Yield | 26.502 | 28.3046 | 15.1482 | 28.7708 | 16.4776 | 18.9873 | 19.3191 | 13.7738 | 21.1613 | 15.6311 | 31.6131 | 24.2881 | 19.9864 | 27.6092 | 35.4026 | 15.2112 | 27.6829 | 27.8692 | 24.9446 | 17.9604 | 16.7247 | 34.2683 | 22.2784 | 24.8761 | 21.4159 | 34.3652 | 19.9446 | 29.287 | 24.3787 | 18.3822 | 24.1105 | 29.5384 | 32.229 | 27.2154 | 36.6246 | 39.9605 | 17.4064 | 19.1751 | 28.1367 | 29.9983 | 25.6549 | 24.6641 | 24.0368 | 25.0619 | 21.0748 | 23.1831 | 23.93 | 27.1174 | 43.7705 | 47.8111 | 24.5914 | 30.377 | 34.5555 | 30.7543 | 27.2668 | 24.2079

## Slide 13: Small Things Add Up
Poor correlation with single variable versus yield.
  What does this mean?
    If you correct a single problem it probably will result in little effect on yield.

## Slide 14
Chart: Observed Yield (bu/ac)
| 26.501999999999999 | 28.304600000000001 | 15.148199999999999 | 28.770800000000001 | 16.477599999999995 | 18.987299999999998 | 19.319099999999999 | 13.7738 | 21.161300000000001 | 15.631099999999998 | 31.613099999999999 | 24.288099999999996 | 19.986399999999996 | 27.609200000000001 | 15.211199999999998 | 27.6829 | 27.869199999999996 | 24.944599999999998 | 17.960399999999996 | 16.724699999999995 | 34.268300000000018 | 22.278399999999998 | 24.876100000000001 | 21.415900000000001 | 34.365200000000002 | 19.944599999999998 | 29.286999999999995 | 24.378699999999991 | 18.382199999999997 | 24.110499999999995 | 29.538399999999996 | 27.215399999999995 | 17.406399999999998 | 19.1751 | 28.136700000000001 | 29.998299999999997 | 25.654900000000005 | 24.036799999999996 | 25.061900000000001 | 21.074800000000003 | 23.1831 | 23.93 | 27.117400000000004 | 47.811099999999996 | 24.5914 | 30.376999999999999 | 34.555500000000002 | 30.754300000000001
 | 27.4688 | 28.3359 | 15.0422 | 23.7157 | 19.1976 | 19.6562 | 20.3258 | 16.7151 | 21.1941 | 17.3074 | 26.354 | 22.929 | 20.4554 | 24.425 | 16.987 | 24.4047 | 25.8297 | 25.7963 | 16.4195 | 20.0022 | 30.7636 | 24.0764 | 22.6347 | 21.4186 | 30.155 | 23.1282 | 29.0144 | 21.9074 | 21.7753 | 24.2248 | 27.2212 | 32.3471 | 14.8479 | 18.2103 | 28.338 | 25.4882 | 26.2535 | 30.2202 | 28.1951 | 29.0041 | 20.955 | 25.8472 | 26.8027 | 47.1329 | 25.701 | 27.9054 | 33.183 | 31.5781

## Slide 15: Other Precision Ag technologies and Soil Assessment
Electrical Conductivity

## Slide 16: Electrical Conductivity
EC is related to soil texture
  Will be influenced by moisture content and will therefore changed over time.
  Will of course be influenced by Salinity
  However, patterns should be consistent.
Can sometimes be related to productivity and/or other soil characteristics such as nutrition or pH.
For better or worse is often used to identify zones for sampling.

## Slide 17: Other on the go sensors
pH, Organic Matter,
http://www.veristech.com/products/visnirfaq.aspx

## Slide 18: Variable Rate N Applications
Important to correct both Spatial and temporal variability
Spatial variability may be dealt with using historic yield maps
Sensors can be
used to address
spatial and
temporal variability
Apply N where
and when needed.

## Slide 19: Variable Rate N Applications
Historically water quality concerns were addressed by decreasing average annual N rates
If not done properly this can reduce yield
Variable rate N applications may not decrease the average N rate but will decrease residual N because N utilization is improved
AKA efficiency is increases, which decreases potential for off-site transport

## Slide 20: Use of Sensor Based N Management in Manured Systems
Sensors have been very much under utilized for manure N management
There is a lot of potential for improving manure N management
Manure N availability is highly variable do to a variety of factors
  Manure type and characteristics
  Soil type, moisture, and temperature
  Application timing and methods
  Crop type (winter vs summer)

## Slide 21: Nitrogen Management in Manured System
Variability in N availability has spawned a great volume of research devoted to evaluating N mineralization and crop uptake.
Despite this effort producers have difficulty dealing with uncertainty about N availably as well as the distribution of available N in the field

## Slide 22: Common Methods to Address Variability
Apply manure at rates that are in excess of crop N need.
Continuous annual application at N based rates
  These solutions have generally been halted by P based nutrient management planning
Apply supplemental N sufficient to overcome variability (apply N sufficient to optimize yield on most N deficient area of the manure field

## Slide 23: Example of Research on Poultry litter N Availability
Poultry litter was pre-plant applied for corn production on the Eastern Shore of VA.
N Source | Total N applied | 2002 | 2003
 | lbs acre-1 | -------bu acre-1----- | 
Peanut Hulls | 125 | 101 | 104
Woodshavings | 125 | 93 | 115
Sawdust (alum) | 125 | 96 | 116
Sawdust | 125 | 97 | 113
Pelletized | 125 | 89 | 120
LSD(p<0.1)= |  | 20 | 15

## Slide 24: N Response Curve
Poultry litter N utilization ranged from 40-56%
Inorganic N Fertilizer Rate (lbs acre-1)
0
50
100
150
200
250
Corn Yield (bu acre-1)
40
60
80
100
120
140
160
2002
2003
2003 Litter
2002 Litter
56%
40%

## Slide 25: In-Field Variability after Manure Applications
Uniform application of manure is difficult to achieve
This will of course cause non uniformity in crop response.
Must be over come by applying based on the need of most deficient areas.

## Slide 26
Study was conducted in Central, KY to evaluate the impact of swine effluent application method on no-till corn yields
Evaluation of Swine Effluent Application Methods
Aeration
Surface Application
Injection

## Slide 27: Spatial Variability In Crop Response Resulting from Application Methods
Surface
Aerway
Injector
Fertilizer
Control
Row 7=210 bu/acre
Row 8=157 bu/acre
Sidedress in 2007
Green seeker was used to measure NDVI and provide row yield estimates

## Slide 28: Actual Corn Yields and Estimated Variability
UAN fertilizer provided lowest variability
Injector optimized yield but maximized between row variation
Surface application had less than optimum yield due to ammonia loss and increased variability
Aeration increased drought stress.
N Source | Total N Applied | Yield | Coefficient of Variation | 
 |  |  | Within Row | Between Row
 |  | bu acre-1 | ---------------%--------------- | 
Check | 0 | 161 | 23 | 4
UAN | 160 | 170 | 20 | 4
Surface | 160 | 159 | 23 | 8
Injector | 160 | 188 | 20 | 8
Airway | 160 | 150 | 25 | 7

## Slide 29: Do Manure Applications Impact Sensor Recommendations for Wheat
Comparison of predicted vs actual wheat yields resulting from pre-plant applications of litter and fertilizer showed that litter use did not influence yield prediction on the Eastern Shore, VA
Chart: Predicted Yield (bu acre-1)
| 99.283574715273915 | 83.567016296575702 | 88.533160361287301 | 89.545217867178934 | 87.907212022809674 | 75.342229354826344 | 90.862395136944414 | 84.120883783631371 | 77.522997759580079 | 65.072907488986758 | 104.59207048458134 | 93.003744493392063 | 89.586674008810562 | 95.380837004405024 | 83.198237885462518 | 73.244162995594706 | 90.775220264317468 | 90.032378854625179
Litter | 74.7658 | 75.5024 | 74.3975 | 77.3439 | 81.3953 | 74.3975 | 75.8707 | 75.1341 | 76.239 | 68.593 | 103.6519 | 85.208 | 90.3001 | 87.1379 | 72.1803 | 74.4107 | 93.3062 | 96.3241
Fertilizer | 82.8685 | 70.3461 | 80.2904 | 85.8149 | 75.8707 | 73.6609 | 65.1899 | 75.1341 | 67.768 | 53.9964 | 71.7531 | 76.2456 | 75.4637 | 93.4624 | 89.081 | 97.2254 | 94.1088 | 108.2075

## Slide 30: Sensor Based Top-dress N Applications Pre-plant Litter
In 2003 yields were similar, however in 2004 litter produced lower yields due to early season N deficiency
Topdress applications did not overcome early season deficiency
-------Treatments†------ |  | 2003 |  | 2004 | 
PP | GS 30 | N Rate | Yield | N rate | Yield
 |  | kg ha-1 | Mg ha-1 | kg ha-1 | Mg ha-1
CHECK | NONE | 0 | 2.6 | 0 | 4.0
Litter | VR | 48-119 | 5.1 | 18-71 | 5.9
Fertilizer | VR | 36-122 | 4.7 | 14-59 | 6.7
lsd (p<0.05) |  |  | 0.8 |  | 1.6

## Slide 31: Sensor-based Technology is a Must for Continued Improvement in Manure N Management
Simply using an N rich strip can take the guess work out of estimating whole field N availability
Provides potential to correct in-field variability with high precision applications (ie, by plant or by row)
Current methods used to estimate crop N status appear to be sufficient